An Overview of  the Design Principles of Drinking Water Chlorination

*1Tochukwu Okeke, 2 Olufunmilayo Ndububa

1Department of Civil Engineering, Federal University Oye-Ekiti, Ekiti State, Nigeria.

2Department of Civil Engineering, Federal University Oye-Ekiti, Ekiti State, Nigeria.

author1_tochukwu.okeke@fuoye.edu.ng|author2_olufunmilayo.ndububa@fuoye.edu.ng

Abstract— The goal of drinking water chlorination is the inactivation of pathogenic organisms in water. It offers the advantage of producing residuals useful for the preservation of water quality in a distribution system. Basic key chlorination concepts include chlorine demand/decay, chlorine residuals, and CT disinfection. The application of these concepts required a good understanding of the hydraulic condition of the system. Important consideration is the determination of initial required chlorine dose. A demonstration model using a public school water supply scheme with an overhead tank is done. This incorporates the kinematic of Contact Time (CT) disinfection, and the application of a demand model for the determination of initial chlorine concentration/dose required. Optimal application of chlorine will prevent incidences of either an over-dose or under-doze which highlight the importance of this study.

Keywords— chlorine demand, CT Disinfection, initial chlorine concentration,  log removal value,  residual concentration.

——————————   (   ——————————

# 1	Introduction

C

hlorine is the most common chemical disinfectant for water treatment (EPA, 2011), and its typical forms include elementary chlorine, hypochlorite and chlorine dioxide. Elemental chlorine is the pure form of chlorine and comes in either a liquid or gaseous state. In its pure form, elementary chlorine is very reactive, volatile and corrosive, and can be flammable when it reacts with ammonia, requiring dilution for safety purposes. Sodium hypochlorite is the diluted form of elementary chlorine and comes in concentration of 12.5 and 15%, while calcium hypochlorite is the solid form and is available in granules, pallets and powder forms (Pennsylvania Department of Environmental Protection, 2016). Its major strength property is that is produces residual which may remain in water even after disinfection has occurred (WHO, 2017).

Disinfection aims at inactivating most of micro-organisms in water essentially the pathogenic ones (Pennsylvania Department of Environmental Protection, 2016). Pathogenic organisms come in form of bacteria, viruses, and protozoa. Important factors that influence their pathogenic activities include: chloride concentration, pH, total organic carbon, dissolved oxygen, hardness, temperature and turbidity (John and Rose, 2005). Survival rate of micro-organism is also an indicator of their resistance to various disinfection methods as determined using a recommended Log Removal Value (LRV). Micro-organism like protozoa with high resistance to chlorine disinfection exhibits high chlorine demand. Chlorination is most effective against bacteria and viruses and least effective against protozoa (WHO, 2017).

Some of the studies on chlorination of drinking water includes: Vasconcelos et al. (1997); Kohpaei and Sathasivan (2011); Casey et al. (2012); and Clark et al. (1989). Vasconcelos et al. (1997) examined chlorine decay within a distribution system using a decay model that incorporates both bulk and wall decay. Kohpaei and Sathasivan (2011) modeled chlorine decay using a parallel second order. The author adopted an analytical approach and found the model as suitable. Casey et al. (2012) examined chlorine demand in water obtained using various treatment method, and observed that the demand pattern follows a power correlation function which contradicts the generally assumed parabolic pattern.

This study therefore adopts the use of a chlorine demand model for the determination of requirement amount of initial chlorine concentration that will be required for appropriate chlorination. Demand model are generally obtained through laboratory experiment, and is a better approach than the trial and error method.

2.  REVIEW OF CHORINATION PRINCIPLES AND FLOW HYDRAULICS

2.1 CT Disinfection

CT is simply the measured chlorine concentration in water multiplied by contact time of chlorine in water (Rush, 2002). The Baffling Factor (B.F) in equation (1) is indicative of variations between plugged and mixed flow, and varies between 0 and 1. The measured concentration is the Residual Free Chlorine (RFC) and is usually determined at the point of the first user, and this mathematically expressed as:

(1)

Where,

is the contact time

B.F is the Baffling Factor

RFC is the Residual Free Chlorine.

Disinfection aims at achieving a target CT level (i.e CTrequired).  CTachieved is the provided CT disinfection in the distribution system while CTrequired is the minimum required CT value for inactivation of the micro-biological organisms in water. The general procedure aims at achieving a deactivation ratio CTachieved/CTrequired ) exceeding 1.0 (Rush 2002). Table 1 is a useful requirement for the determination of CTrequired. Relevant control variable are temperature, pH and residual concentration. Model (1) presents a useful formulation for the determination of CTachieved. Model equation (2) presents an alternative to (1), and is based on infectivity data (LeChevallier and Kwok-Keung Au., 2004) for Giardia inactivation. This was proffered by Clark, et al., (1989):

(2)

Where,  is the disinfectant residual concentration, and  is the reaction temperature in degrees Celcius.

Table 1. CT table (EPA, 2011)

2.2 Log Removal Value (LRV)

The Log Reduction Value is expressed as the ability of a treatment processes to remove pathogenic microorganisms. High LRVs will automatically require higher CT values. LRVs are categorised according to the different pathogen type e.g LRV for virus, bacteria, and protozoa. This value is determined in the laboratory using equation (3). An LRV of 1 is equivalent to 90% removal of a target pathogen, an LRV of 2 is equivalent to 99% removal and an LRV of 3 is equivalent to 99.9% removal and so on (WRA, 2014; USEPA, 2012).

(3)

Many water treatment uses giardia and virus inactivation requirement as standard for water treatment. Table 2 shows a giardia log reduction based on the number of cryst per 100L of obtained. A Giardia 3-log removal generally requires a higher CT value than that for a 2-log. Chlorination is generally most effective against bacteria and viruses and least effective against protozoa (WHO, 2017), and therefore protozoa requirement becomes the critical value. Chlorination technically is not expected to satisfy the full LRV requirement as other treatment process like filtration, sedimentation and coagulation contribute significantly.

Table 2.  Required level of giardia log reduction

| S/n | Raw water level | Recommended giardia log reduction |
| --- | --- | --- |
| 1 | <1 cryst per 100 litres | 3-log |
| 2 | 1 cryst/100L -10cysts/100L | 3-log to 4-log |
| 3 | 10 cryst/100L – 100cyst/100L | 4-log to 5-log |
| 4 | >100 cryst/100L | >5-log |

Source: Rush, 2002.

2.3 Chlorine Demand

Demand models measures the “chlorine consumption rate” in water over time. The initial added chlorine initially reacts in three ways: (1) irreversibly with manganese, iron and hydrogen sulphide, (2) reversibly with organic matter and ammonia, (3) with water. The reversible reaction in step (2) results in combined chlorine in form of chloramines, while the left over that reacts with water is the RFC. These organic and the inorganic components “eat up” chlorine in water, before leaving residual free chlorine useful for the disinfection treatment of microbial in water. This demand must be satisfied to ensure adequate biocidal treatment. Chlorine demand increases as the RFC decreases, and can be mathematical expressed as:

(4)

Fig 1 Breakpoint chlorination

The other approaches requires: (1) breakpoint chlorination (Fig 1) and (2) Chlorine demand model equation (5). Chlorine demand is also measured as the portion in Fig 1, where the combined chlorine residuals predominate, i.e before the rise of the RFC portion of the curve. The model approach adopted for this study follows the power law correlation model (Casey et al. 2012), expressed as:

(5)

Where  is chlorine demand measured in mg/l,  is contact time (mins),   and   are empirical fitted coefficient.

2.4 Residual Free Chlorine (RFC)

RFC is portion available for disinfection and is the strong from (Wiant, 2013; Pennsylvania Department of Environmental Protection, 2016). Addition of free chlorine and combined chlorine results in total chlorine. Different test indicators are used in the laboratory to determine the concentration level of both total and free chlorine. To achieve microbial inactivation, the concept of free chlorine residual-time relationship plot must be determined using either a demand or decay curve. Chlorine residual has the advantage of remaining for a longer period of time in a distribution network when compared to ozone which easily decompose but have stronger oxidizing power (National Academy of Sciences, 1977).

Residual concentration in a distribution system is required at recommended level to prevent possible re-contamination of the flowing water through pipe wall bio-film.

2.5 Hydraulic Considerations

2.5.1 Contact time

Various microbes in water require different chlorine contact time period for effective disinfection. Adequate contact time must be provided before the water gets to the first consumer. Determination of contact time incorporates the hydraulic flow condition in the tank or pipe network. An ideal Contact time for plugged flow through a conduit pipe network is generally expressed as:

(6)

In a real distribution system, this ideal model equation (6) is not suitable for contact tanks since flow through it falls between fully mixed and plug flow. This requires determining the Residence Time Distribution (RTD). EPA, (1999) guideline requires a “Correction Factor (C.F)” or “Baffling Factor (B.F)” which is based on t10 value .Table 3 shows the baffling factors for different tank conditions, while equation (7) shows hydraulic contact time expression incorporating B.F suitable for contact tank.

Table 3. Contact tank baffling factor description

| S/n | Condition |  | Description |
| --- | --- | --- | --- |
| 1 | Unbaffled | 0.1 | None, agitated Basin, very low length to widith ratio, high inlet and outlet velocities |
| 2 | Poor | 0.3 | Single or multiple unbaffled inlet and outlet, no intra-basin baffles |
| 3 | Average | 0.5 | Baffled inlet and outlet with some intra-basin baffles |
| 4 | Superior | 0.7 | Perforated inlet baffle, serpentine or perforated intra-basin baffles, outlet weir or perforated laundaries |
| 5 | Perfect | 1.0 | Very high length to width ration (pipeline flow) |

Source: EPA 2011.

(7)

2.5.2 Water demand estimates

This is expressed as the water quantity utilized daily by individual. Factors considered include economic, demographic, weather, and population growth. Water demand estimate is fundamental to the determination of tank size and flow rates. Volumetric flow rates derived using water demand estimate is shown in equation (8).

(8)

2.6  Chlorine Dozing

The expression in (9) shows a typical demand curve with the empirical fitted coefficients determined (Casey et al. 2012). This follows the power law correlation model (5). The treatment category is the chemical coagulation/clarification/filtration of a conventional treatment process. This is a common treatment procedure in many conventional treatment plants, and therefore is adopted for this study.

(9)

The initial chlorine dose  is the amount of chlorine initially added to the distribution system for disinfection purpose and was determined for demonstration model in this study using equation (12).

(12)

3.	DESIGN METHODOLOGY

3.1   Hydraulic Considerations

This model considers a treatment tank at elevation +10m above datum level. An elevation height of 10 meters is expected to provide sufficient hydraulic head for effective water distribution. Hydraulic consideration includes:

- Determination of required Flowrate: This was determined based on equation (8).

- Determination of appropriate tank size: This was determined as allowing thrice refilling each day.

- Determination of Contact time: Model expression (9) and (10) are useful for this purpose.

3.2   Determination of CT required and CT achieved.

Procedural steps using tables and charts are as follows (Rush, 2002):

- Determining of required CT:  A predetermined LRV of 3 log inactivation was adopted. Table 1 was used for determination of required CT . Similar tables exist for  bacteria and virus disinfection, and can be obtained in EPA, (2011).

- Determining of achieved CT: Relevant models equations include (1), (2), (6) and (7).

- Comparing CT Values: If CTacheived > CTrequired, then you will have met your disinfection requirement.

3.2  Chlorine Demand

Model equation (9) was used for this purpose with a pH value of 6.73 and temperature 15oC.

3.3  Model Design

Relevant hydraulic design data useful for this design is presented in Table 4.

| No | Hydraulic parameters | Value |
| --- | --- | --- |
| 1 | Water demand (W.D) | 135liters/capita/day |
| 2 | Capacity Factor (C.F) | 1.5 |
| 3 | Peaking Factor (P.F) | 2.5 |
| 4 | Baffling Factor (B.F) | 0.3 |
| 5 | Design population size | 2000 |
| 6 | Hourly Flow rate (based on (8)) | 16.88 |

4.	DESIGN RESULT AND DISCUSSION

Table 5.0 shows the required tank size for a population of 2000 people with an option of thrice filling of the tank daily.

Table 5.  Designed Tank Size for a Population Size of 2000.

| S/n | Population Size | Capacity Factor | Water Use | Tank Size (litres) | Tank Dimension |
| --- | --- | --- | --- | --- | --- |
| 1 | 2000 | 1.5 | 270,000 | 135,000 | 7.0 x 5.0 x 3.8 |

Source: Author

4.1  Practice Design for 4-Log Virus Inactivation

1) The CTrequired for 4-log inactivation of virus at temperature of 15oC and pH range of 6.73 is 4   mgmimL-1 (EPA, 1991).

2) The CTachieved is shown in Table 6 for RFC range of 0.2mg/L to 0.5mg/L.

Table 6. Viral Inactivation Data for Residual Concentration Range of 0.2 to 0.5mg/L

| S/n | RFC (mg/L) | CT achieved | CT required | Ratio | Virus Inactivation |
| --- | --- | --- | --- | --- | --- |
| 1 | 0.2 | 29 | 4 | 7 | Satisfactory |
| 2 | 0.3 | 43 | 4 | 10 | Satisfactory |
| 3 | 0.4 | 59 | 4 | 14 | Satisfactory |
| 4 | 0.5 | 72 | 4 | 18 | Satisfactory |

3) Based on inactivation ratio for 4-Log inactivation shown in (13), this design satisfies the viral inactivation requirement.

4-log virus inactivation = inactivation ratio x 4 ≥ 4			(13)

4) The required initial concentration is shown in Table 7.

Table 7. Required Initial chlorine concentration  for residual range of 0.2 to 0.5 mg/L

| S/n | Contact Time (t) |  | RFC (mg/L) | Chorine demand |  |
| --- | --- | --- | --- | --- | --- |
| 1 | 143 |  | 0.2 | 1.4 | 1.6 |
| 2 | 143 |  | 0.3 | 1.4 | 1.7 |
| 3 | 143 |  | 0.4 | 1.4 | 1.8 |
| 4 | 143 |  | 0.5 | 1.4 | 1.9 |

4.2  Practice Design for 3-Log Giardia  Inactivation

1) The CTrequired for 3-log inactivation of Giardia at temperature of 15oC and pH range of 6.73 for the different RFC’s is shown in Table 8.

2) The CT achieved was determined using (2) and (7) indicates an inactivation ratio as satisfactory.

Table 8: 3-log Giardia Inactivation Data for Residual Concentration Range of 0.4 to 1.0 mg/L

| S/n | B.F | Contact Time (t) | RFC (mg/L) | CT achieved | CT required | Ratio | Giardia Inactivation |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.3 | 143 | 0.4 | 59 | 59 | 1.0 | Satisfactory |
| 2 | 0.3 | 143 | 0.5 | 72 | 60 | 1.2 | Satisfactory |
| 3 | 0.3 | 143 | 0.8 | 114 | 61 | 1.9 | Satisfactory |
| 4 | 0.3 | 143 | 1.0 | 143 | 63 | 2.3 | Satisfactory |

3) The required initial dosage for the different residuals are shown in Table 9.

Table 9. Required Initial chlorine concentration  for residual range of 0.4 to 1.0 mg/L

| S/n | Contact Time (t) | RFC (mg/L) | Chorine demand |  |
| --- | --- | --- | --- | --- |
| 1 | 143 | 0.4 | 1.4 | 1.8 |
| 2 | 143 | 0.5 | 1.4 | 1.9 |
| 3 | 143 | 0.8 | 1.4 | 2.2 |
| 4 | 143 | 1.0 | 1.4 | 2.4 |

4.3	 Discussion

For the viral inactivation, high values of inactivation ratios were observed indicative of high efficiency in the disinfection process. Therefore the residence time of chlorine in the water is adequate provide the needed CT disinfection.

The same chlorine demand was observed for both viral and gardia inactivation. This is because both have: same contact time, same log requirement, and same tank size. Therefore in other to satisfy the higher CT requirement for gardia inactivation for hydraulic contact time within the tank, higher residual concentration was observed.

Though satisfactory, additional contact time or a higher residaul target should be provided for the inactivation with a ratio of 1.0 and a residual of 0.4 mg/L in Table 8. This is because at any slight lower CT, disinfection will not be satisfactory. Additional contact time can alos be achieved within the pipeline before the first user, or alternatively allowing the water to stay for a longer period in the contact tank.

Higher level of initial concentration was observed for gardia inactivation since it has a higher CT requirement.

6.  CONCLUSION

The study has demonstrated the usefulness of chlorine demand model for the determination of initial required chlorine concentration. Chlorine demand models are generally determined through laboratory experiment.

7. REFERENCES

Ale, P.O., Aribisala, J.O., Awopetu, M.S. (2015). Evaluation of Yeild of Wells in Ado-Ekiti, Nigeria. IISTE Journal, Vol 7, No 11.

Army-Air Force.(1985). Water Supply, Water Storage. Technical Manual. Joint Department of Army and Air Force, USA. TM 5-813-4/AFM 88-100, Vol 4.

Casey T., Kearney, & P.,Kerr, H. (2012). The Chlorine Demand Characterization of Irish Water Supplies: Process Design Implication for Disinfection and THM Formation. CIWEM2012/CDS/WS.

Clark, R.M., Read, E.J., & Hoff, J.C. (1989). Analysis of Inactivation of Giardia Lamblia by Chlorine. Journal of Engineering Division of the ASCE. 115(1), 80-90.

Clark, R.M  (1998). Chlorine Demand and TTHM Formation Kinetics: a Second-Order Model. J. Environ. Eng. 1998.124:16-24.

EPA (1991). Guidiance Manual for Compliance with the Filteration and Disinfection Requirement for Public Water System using Surface Water Sources. Environmental Protection Agency (EPA) Office of Drinking Water, Criteria and Standard Division, Science and Technology Branch, Washington, DC.

EPA (2001). Controlling Disinfection By-Products and Microbial Contamination in Drinking Water. Environmental Protection Agency (EPA) Office of Research and Development, Washington, D.C.

EPA (2011). Water Treatment Manual: Disinfection. Environmental Protection Agency (EPA) Office of Environmental Enforcement, Ireland.

Farovitch, Lorne (2016) Survival of Various Pathogenic Microorganisms in Surface Waters and Sediments in Western New York" Thesis. Rochester Institute of Technology.

Indian Standard. (1993). Code of Basic Requirement for Water Supply, Drainage and Sanitation. Public Health Engineering. IS_1172 (1993). Fourth Edition.

John,  D.E & Rose, J.B (2005) Review of Factors Affecting Microbial Survival in Groundwater. Environmental Science & Technology, Vol. 39, (19), 2005, Pg 7345 to 7356.

Kohpaei, J.A and Sathasivan, A (2011) Chlorine Decay Prediction in Bulk Water Using the Parallel Second Order Model: An Analytical Solution Development.  Chemical Engineering Journal. In-press.

LeChevallier, M. K., and Kwok-Keung Au. (2004) Water Treatment and Pathogen Control: Process Efficiency in Achieving Safe Drinking Water. World  Health Organisation (WHO). Published by IWA Publishing, London, UK.

National Academy of Sciences (1980): Drinking Water and Health, Volume 2 Safe Drinking Water Committee, Board on Toxicology and Environmental Health Hazards, Assembly of Life Sciences. 408 pages

National Academy of Sciences. (1977) Drinking Water and Health, Volume 2. Safe Drinking Water Committee, National Academy of Sciences, Washington, D.C. 939 pp.

Netshidaulu, A.H. (2015). Impact of Chlorine and Wastewater Contact Time, Chlorine Residual and Mixing on Microorganism Inactivation. An Msc Reasearch Report for the Award of a Degree of Master of Science in Civil Engineering.

Pennsylvania Department of Environmental Protection., (2016). Module 5: Disinfection and Chlorination.. Bureau of Safe Drinking Water, Department of Environmental Protection. Waste Treatment Plant Operator Certification Training.

Rush, B. (2002). CT Disinfection Made Simple. A Presentation for the Alberta Water and Wastewater Operator’s Association Annual Conference in Banff, Alberta.

USEPA. (2012). Review of Inactivation by Disinfection for SDWA Primacy Agencies.

United States Environmental Protection Agency (USEPA) Office of Groundwater and Drinking Water.

Vasconcelos, J J.,  Rossman, L A.,  Grayman WM.,  Boulos, PF., Clark R.M., 1997. Characterization and modeling of Chlorine Decay in distribution Systems. Journal AWWA. Volume 89 Issue 7.Pg 54 – 65.

WHO (2017). Principles and Practices of Drinking Water Chlorination. A Guide to Strengthening Chlorination Practices in Small- to Medium-Sized Water Supplies. World Health Organization (WHO) Regional Office of South East Asia.

## Wiant, C. (2013). The Chlorine Residual: A Public Health Safeguard. Water Quality and Health Council. Avaliable online @ https://waterandhealth.org/healthy-pools/chlorine-residual-public-health-safeguard/. Accessed on 04/06/2018.

WRA. (2014). Fact Sheet: Log Removal Values in Waste Water Treatment. Water Research Australia (WRA) Water for the WellBeing of All Australians.

his document is a template for Microsoft Word versions 6.0 or later. You can use it to prepare your manuscript. Then type over sections of the document or cut and paste from another document and then use markup styles. Please keep the template as it is. Do not reset the template into any other format or paper size.

Highlight a section that you want to designate with a certain style, and then select the appropriate name on the style menu. The style will adjust your fonts and line spacing. Use italics for emphasis; do not underline (Kong et al., 2011; Young, Roy, & Young, 2007). Do not change the font sizes or line spacing to squeeze more text into a limited number of pages. Please be certain to follow all submission guidelines when formatting an article or it will be returned for reformatting.

FUOYEJET staff will confirm and complete the final formatting of your paper.

# 1	Introduction

T

his document is a template for Microsoft Word versions 6.0 or later. You can use it to prepare your manuscript. Then type over sections of the document or cut and paste from another document and then use markup styles. Please keep the template as it is. Do not reset the template into any other format or paper size.

Highlight a section that you want to designate with a certain style, and then select the appropriate name on the style menu. The style will adjust your fonts and line spacing. Use italics for emphasis; do not underline (Kong et al., 2011; Young, Roy, & Young, 2007). Do not change the font sizes or line spacing to squeeze more text into a limited number of pages. Please be certain to follow all submission guidelines when formatting an article or it will be returned for reformatting.

FUOYEJET staff will confirm and complete the final formatting of your paper.

# 2 Procedure for Paper Submission

## 2.1 Review Stage

Detailed submission guidelines can be found on the ‘guide for authors’ (GfA) available from the  web pages of FUOYEJET. All authors are responsible for understanding these guidelines before submitting their manuscript. For further information on both submission guidelines, authors are strongly encouraged to refer to http://engineering.fuoye.edu.ng/journal.

The details of all submission requirements must be according to the specified rules and guidelines stipulated within the ‘GfA’.

## 2.2 Final Stage

For papers accepted for publication, it is essential that the electronic version of the manuscript and artwork match the hardcopy exactly! The quality and accuracy of the content of the electronic material submitted is crucial since the content is not recreated, but rather converted into the final published version.

*Corresponding Author

All papers in FUOYEJET are edited electronically. A final submission materials check list, transmission and compression information, and general publication materials can be found at: http://engineering.fuoye.edu.ng/journal.

## 2.3 Figures

All figures will be processed as images. You need to embed the images in the paper itself. Please don’t send the images as separate files.

# 3	Sections

As demonstrated in this document, the numbering for sections upper case Arabic numerals, then upper case Arabic numerals, separated by periods. Initial paragraphs after the section title are not indented. Only the initial, introductory paragraph has a drop cap.

# 4	Citations

FUOYEJET style is APA IV referencing format. Place citations in individual brackets, followed by a comma, e.g. (Balogun & Mativenga, 2013) References must be fully documented and organized strictly in the APA (American Psychological Association) style; this is similar to the Harvard style of referencing. References should relate only to material cited within the manuscript and be listed in alphabetical order at the end of each manuscript. Please refer to the GfA for further informations. Start a new cited statement as the following paragraph.

Adeniyi et al. (2016) reported the neural and behavioural changes in male periadolescent mice …. When citing a section in a book, please give the relevant page numbers.

# 5	Equations

If you are using Word, use either the Microsoft Equation Editor or the MathType add-on (http://www.mathtype.com) for equations in your paper (Insert | Object | Create New |Microsoft Equation or MathType Equation). “Float over text” should not be selected.

Number equations consecutively with equation numbers in parentheses flush with the right margin, as in (1). First, use the equation editor to create the equation. Then, select the “Equation” markup style. Press the tab key and write the equation number in parentheses. To make your equations more compact, you may use the solidus ( / ), the exp function, or appropriate exponents. Use parentheses to avoid ambiguities in denominators. Punctuate equations when they are part of a sentence, as in

(1)

Be sure that the symbols in your equation have been defined before the equation appears or immediately following. Italicize symbols (T might refer to temperature, but T is the unit tesla). To refer to any equation in-text, please refer to ‘equation (1),’ and at the beginning of a sentence: “Equation (1) shows ... .”

Please note that math equations might need to be reformatted from the original submission for page layout reasons. This includes the possibility that some in-line equations will be made to display equations to create better flow in a paragraph. If display equations do not fit in the two-column format, they will also be reformatted. Authors are strongly encouraged to ensure that equations fit in the given column width.

# 6	Helpful Hints

## 6.1	Figures and Tables

Figures and tables should be sized as they are to appear in print. Figures or tables not correctly sized will be returned to the author for reformatting.

Place figure captions below the figures; place table titles above the tables. If your figure has two parts, include the labels “(a)” and “(b)” as part of the artwork. Please verify that the figures and tables you mention in the text actually exist. Figures and tables should be called out in the order they are to appear in the paper. For example, avoid referring to figure “8” in the first paragraph of the article unless figure 8 will again be referred to after the reference to figure 7. Please do not include figure captions as part of the figure. Do not put captions in “text boxes” linked to the figures. Do not put borders around the outside of your figures. Do not abbreviate “Table.” Tables are numbered numerically.

All graphics will appear in print as black and white, but coloured equivalent might appear in online version. Ensure all graphics will shows correctly when printed in grayscale.

Figure axis labels are often a source of confusion. Use words rather than symbols. As an example, write the quantity “Magnetization,” or “Magnetization M,” not just “M.” Put units in parentheses. Do not label axes only with units. As in Fig. 1, for example, write “Magnetization (A/m)” or “Magnetization (Am(1),” not just “A/m.” Do not label axes with a ratio of quantities and units. For example, write “Temperature (K),” not “Temperature/K.” Table 1 shows some examples of units of measure.

Multipliers can be especially confusing. Write “Magnetization (kA/m)” or “Magnetization (103 A/m).” Do not write “Magnetization (A/m) ( 1,000” because the reader would not know whether the top axis label in Fig. 1 meant 16,000 A/m or 0.016 A/m. Figure labels should be legible, approximately 8 to 12 point type. When creating your graphics, especially in complex graphs and charts, please ensure that line weights are thick enough that when reproduced at print size, they will still be legible. We suggest at least 1 point.

## 6.3	Footnotes

It is recommended that footnotes be avoided; instead, try to integrate the footnote information into the text.

## 6.4	Lists

The FUOYEJET style is to create displayed lists if the number of items in the list is longer than three. For example, within the text lists would appear 1) using a number, 2) followed by a close parenthesis. However, longer lists will be formatted so that:

- Items will be set outside of the paragraphs.

- Items will be punctuated as sentences where it is appropriate.

- Items will be numbered, followed by a period.

## 6.5	Theorems and Proofs

Theorems and related structures, such as axioms corollaries, and lemmas, are formatted using a hanging indent paragraph. They begin with a title and are followed by the text, in italics.

Theorem 1. Theorems, corollaries, lemmas, and related structures follow this format. They do not need to be numbered, but are generally numbered sequentially.

Proofs are formatted using the same hanging indent format. However, they are not italicized.

Proof. The same format should be used for structures such as remarks, examples, and solutions (though these would not have a Q.E.D. box at the end as a proof does).

Table 1. Units for Magnetic Properties

Statements that serve as captions for the entire table do not need footnote letters.

aGaussian units are the same as cgs emu for magnetostatics; Mx = maxwell, G = gauss, Oe = oersted; Wb = weber, V = volt, s = second, T = tesla, m = meter, A = ampere, J = joule, kg = kilogram, H = henry.

# 7	End Sections

## 7.1	Appendices

Appendixes, if needed, appear before the acknowledgment. In the event multiple appendices are required, they will be labeled “Appendix A,” “Appendix B, “etc. If an article does not meet the submission length requirements, authors are strongly encouraged to make their appendices supplemental material.

## 7.2	Acknowledgement

Authors should acknowledge all contributors to the research. Use the singular heading even if you have many acknowledgments. Avoid expressions such as “One of us (S.B.A.) would like to thank ... .” Instead, write “F. A. Author thanks .. .” Sponsor and financial support acknowledgements are included in the acknowledgement section. For example: This work was supported in part by the TETFUND under Grant NG123456 (sponsor and financial support acknowledgement goes here). Researchers that contributed information or assistance to the article should also be acknowledged in this section.

## 7.3	References

Reference list should be at the end of the paper using the APA “References” style. See the FUOYEJET’s style for reference formatting. The order in which the references are submitted in the manuscript is the order they will appear in the final paper, i.e., references submitted non-alphabetized will remain that way.

Please note that the references at the end of this document are in the preferred referencing style. Within the text, use “et al.” when referencing a source with more than three authors. In the reference section, give all authors’ names; do not use “et al.” Papers that have not been published should be cited as “unpublished” with APA referencing styles. Papers that have been submitted or accepted for publication should be cited as “submitted for publication”. Please give affiliations and addresses for personal communications ( Balogun, Kirkwood, & Mativenga, 2014).

Capitalize all the words in a paper title. For papers published in translation journals, please give the English citation first, followed by the original foreign-language citation (Balogun, Aramcharoen, Mativenga, & Chuan, 2013). The sensor based synergy (Chen, Hoey, Nugent, Cook, & Yu, 2012).

## 7.4	Additional Formatting and Style Resources

Additional information on formatting and style issues can be obtained in the FUOYEJET ‘GfA’ and Style Guide, availabe on our website.

# 8	Conclusion

Although a conclusion may review the main points of the paper, do not replicate the abstract as the conclusion. A conclusion might elaborate on the importance of the work or suggest applications and extensions. Authors are strongly encouraged not to call out multiple figures or tables in the conclusion—these should be referenced in the body of the paper.

Acknowledgment

The authors wish to thank A, B, C. This work was supported in part by a grant from XYZ.

References

Adeniyi, P. A., Ishola, A. O., Laoye, B. J., Olatunji, B. P., Bankole, O. O., Shallie, P. D., & Ogundele, O. M. (2016). Neural and behavioural changes in male periadolescent mice after prolonged nicotine-MDMA treatment. Metabolic brain disease, 31(1), 93-107.

Balogun, V. A., Aramcharoen, A., Mativenga, P. T., & Chuan, S. K. (2013). Impact of Machine Tools on the Direct Energy and Associated Carbon Emissions for a Standardized NC Toolpath Re-engineering Manufacturing for Sustainability (pp. 197-202): Springer.

Balogun, V. A., Kirkwood, N. D., & Mativenga, P. T. (2014). Direct Electrical Energy Demand in Fused Deposition Modelling. Procedia CIRP, 15, 38-43.

Balogun, V. A., & Mativenga, P. T. (2013). Modelling of direct energy requirements in mechanical machining processes. Journal of Cleaner Production, 41, 179-186.

Chen, L., Hoey, J., Nugent, C. D., Cook, D. J., & Yu, Z. (2012). Sensor-based activity recognition. IEEE Transactions on Systems, Man, and Cybernetics, Part C (Applications and Reviews), 42(6), 790-808.

Kong, D., Choi, S., Yasui, Y., Pavanaskar, S., Dornfeld, D., & Wright, P. (2011). Software-based tool path evaluation for environmental sustainability. Journal of Manufacturing Systems, 30(4), 241-247. doi: 10.1016/j.jmsy.2011.08.005

Young, J., Roy, H. S., & Young, J. (2007). Transforming server-side processing grammars: Google Patents.

# Text boxes

Fig. 1. Magnetization as a function of applied field. Note that “Fig.” is abbreviated. There is a period after the figure number, followed by one space..